Digital Watchdog® is a leading manufacturer of security and surveillance solutions, offering stunning image quality, advanced hardware capabilities, reliable customer support and lowest total cost of deployment to the analog & IP megapixel surveillance markets. Located in Cerritos, CA with manufacturing facilities in Seoul, Korea, Digital Watchdog® is committed to delivering powerful security solutions to its customers worldwide.

For additional information, contact:

# Digital Watchdog®
	16220 Bloomfield Avenue,

# Cerritos, California 90703 USA

# Phone: +1 888 446-3593

# Web: www.digital-watchdog.com

# E-mail: dw-tech@digital-watchdog.com

Blackjack® Rack™ SERVER

# DIVISION 28 – ELECTRONIC SAFETY AND SECURITY (MasterFormat 2016)

28 05 00 	Common Work Results

28 05 19 	Storage Appliances for Electronic Safety and Security

28 05 19.15	Network Video Recorders

Notes to Specifier:

1.  Where several alternative parameters or specifications exist, or where, the specifier has the option of inserting text, such choices are presented in <bold text>.

2.  Explanatory notes and comments are presented in colored text.

3. CSI MasterFormat 2016 incorporates numerous significant changes affecting electronic safety and security. This document is written to provide flexibility in using either format, although adoption of MasterFormat 2016 is encouraged. The following is a guide to the MasterFormat numbers relevant to the product referenced in this specification.

4. MasterFormat 2014 Specification Category: 28 23 00- Video Surveillance

Blackjack® Rack™ Server

- GENERAL

  - SUMMARY

    - Section includes a rack mounted network video recorder with embedded IP VMS.

    - Product - A 19” rack mount network video recording system with embedded video management software, providing available storage up to 288  TB at a data transfer rate of up to 600 Mbps, with 30 fps frame rates.

## Related Requirements

      - 27 11 16 – Communications Cabinets, Racks, Frames, and Enclosures

      - 27 15 01.13 – Video Surveillance Communications Conductors and Cables

      - 28 05 03 - Safety and Security Network Communications Equipment

      - 28 05 15 - Servers for Electronic Safety and Security

      - 28 05 17 - Workstations for Electronic Safety and Security

      - 28 06 20 - Schedules for Video Surveillance

      - 28 20 00 - Video Surveillance

  - REFERENCES

    - Abbreviations

      - CPU – Central Processing Unit

      - fps - frames per second

      - HTTP - Hypertext Transfer Protocol

      - IP - Internet Protocol

      - JPEG - Joint Photographic Experts Group

      - MAC – Media Access Control

      - MJPEG - Motion JPEG

      - MPEG - Moving Pictures Experts Group

      - NVR – Network Video Recorder

      - PTZ – Pan, Tilt, and Zoom

      - RADASS – Resolution and Algorithmic Data Adaptive Scaling System

      - RTP - Real-Time Transport Protocol

      - RTSP - Real-Time Streaming Protocol

      - SSD – Solid State Drive

      - TB - Terabyte

      - UI –User Interface

      - VMS - Video Management System

    - Definitions

      - E-mapping – Images that can be used as a background in client software to show server and camera placement at a site.

      - Media Server – A server/controller for cameras and network connections including client connections and camera stream encoding to hard disks. A Server may function as a Media Server.

      - Motion sensitivity – Degree of pixelization change in a selected area of the video scene required to trigger a recording or alarm.

    - Reference Standards

      - Network

        - IEEE - 802.3 Ethernet Standards

      - Video

        - ISO / IEC 14496 – MPEG-4

          - ISO / IEC 14496–10, MPEG-4 Part 10 ( ITU H.264)

        - ISO / IEC 10918 – JPEG

        - ONVIF – Profile S

  - SUBMITTALS

    - Product Data

      - Manufacturer’s printed or electronic data sheets

      - Manufacturer’s installation and operation manuals

      - Warranty documentation

  - QUALIFICATIONS

    - Manufacturer shall have a minimum of five years’ experience in producing IP video equipment and software.

    - Installers shall be trained and authorized by the Manufacturer to install, integrate, test, and commission the video system.

  - LICENSE AND SUPPORT

    - Licenses issued by the Manufacturer for camera recording shall not expire for the life of the camera.

    - The product shall include eight (8) user licenses.

  - WARRANTY

    - The product shall carry a five (5) year warranty with on-site, Next Business Day**, Keep Your Hard Drive warranty to ensure peace of mind. (** after remote diagnosis).

END OF SECTION

- PRODUCTS

  - EQUIPMENT

    - Manufacturer: 	Digital Watchdog, Inc.

16220 Bloomfield Avenue. Cerritos,

California USA 90703 USA

Phone: (866) 446-3595

Web: www.digital-watchdog.com

E-mail:  dw-tech@digital-watchdog.com

    - Model: DW-BJRR2XxxT

Digital Watchdog model differences:

DW-BJRR2X208T - 208TB internal storage, 192TB with RAID5, 176TB with RAID6, Windows OS

DW-BJRR2X208TS - 208TB internal storage, 192TB with RAID5, 176TB with RAID6, Windows Server OS

DW-BJRR2X208TLX - 208TB internal storage, 192TB with RAID5, 176TB with RAID6, Linux OS

DW-BJRR2X224T - 224TB internal storage, 208TB with RAID5, 192TB with RAID6, Windows OS

DW-BJRR2X224TS - 224TB internal storage, 208TB with RAID5, 192TB with RAID6, Windows Server OS

DW-BJRR2X224TLX - 224TB internal storage, 208TB with RAID5, 192TB with RAID6, Linux OS

DW-BJRR2X240T - 240TB internal storage, 224TB with RAID5, 208TB with RAID6, Windows OS

DW-BJRR2X240TS - 240TB internal storage, 224TB with RAID5, 208TB with RAID6, Windows Server OS

DW-BJRR2X240TLX - 240TB internal storage, 224TB with RAID5, 208TB with RAID6, Linux OS

DW-BJRR2X256T - 256TB internal storage, 240TB with RAID5, 224TB with RAID6, Windows OS

DW-BJRR2X256TS - 256TB internal storage, 240TB with RAID5, 224TB with RAID6, Windows Server OS

DW-BJRR2X256TLX - 256TB internal storage, 240TB with RAID5, 224TB with RAID6, Linux OS

DW-BJRR2X272T - 272TB internal storage, 256TB with RAID5, 240TB with RAID6, Windows OS

DW-BJRR2X272TS - 272TB internal storage, 256TB with RAID5, 240TB with RAID6, Windows Server OS

DW-BJRR2X272TLX - 272TB internal storage, 256TB with RAID5, 240TB with RAID6, Linux OS

DW-BJRR2X288T - 288TB internal storage, 272TB with RAID5, 256TB with RAID6, Windows OS

DW-BJRR2X288TS - 288TB internal storage, 272TB with RAID5, 256TB with RAID6, Windows Server OS

DW-BJRR2X288TLX - 288TB internal storage, 272TB with RAID5, 256TB with RAID6, Linux OS

    - Alternates: 		None

  - NETWORK VIDEO RECORDER

    - The Network Video Recorder (“NVR”) shall be a 19” 2U rackmount video recording system and IP Video Management System Media Server.

    - Performance

      - The NVR shall be able to record dual video streams at an aggregate data rate of 600 Mbps.

      - Resolution:			HD 1080p

      - Number of remote clients:	unlimited

    - Operating System: 			Windows 10 IoT, Ubuntu Linux, Windows Server OS

Digital Watchdog model differences:

DW-BJRR2XxxT	Windows® 10 IoT OS

DW-BJRR2XxxTLX	Linux® Ubuntu® OS

DW-BJRR2XxxTS	Windows Server® OS

      - Dedicated Storage:		2 x 240GB M.2 SSD (RAID1)

    - Hardware

      - Storage

        - Total available raw storage: 	Up to raw 288 TB

        - Number of Drives:		18x SAS HDD

        - RAID: 			RAID5, RAID6

      - Processor:  			2x Intel Xeon Silver processors

      - Memory: 			32GB (4x 8GB)

      - Power Supply:			Dual 1100 W redundant

      - Video

        - Graphics card:		NVIDIA T400 2GB

        - Interfaces:			3 x mini DisplayPort (1 x mini-DP to true HD adapter included)

      - Additional Interfaces

        - USB			2.0 USB ports

3.0 USB ports

        - Serial Port

        - Ethernet Ports:		6x 1GB Base-T Ethernet Ports,

2x 10G SFP+ Fiber

iDRAC9 Enterprise

      - Certification: 			UL listed, CE, FCC, ONVIF, NDAA, TAA

      - Operating Temperature: 	41o ~ 104o F (5o ~ 40o C) / 5~85% RH

      - Dimensions (L x W x H):	 	17.6” x 31.9” x 3.41” (447.04 x 810.26 x 86.61mm)

END OF SECTION

- EXECUTION

  - INSTALLERS

    - Contractor personnel shall comply with all applicable state and local licensing requirements.

    - Contractor personnel shall be factory trained and certified to install, service and maintain the system.

## PREPARATION

## Camera and encoder compatibility shall be verified prior to deployment.

## The network design and configuration shall be verified for compatibility and performance with the IPVMS.

## Network configuration shall be tested and qualified by the Contractor prior to camera installation.

  - INSTALLATION

    - Contractor shall follow all Manufacturer published installation procedures and guidelines.

    - Products shall be installed in areas consistent with Manufacturer recommendations.

END OF SECTION